## Slide 1: Computer vision driving aids an adaptation of adas to the android platform
Traffic sign recognition
Lane departure detection and warning
Collision and obstacle avoidance

## Slide 2: Team members
Belorkar, Sapana Senior Quality Assurance Engineer, Insurance Industry
Burbidge, Adam (Team Leader) Systems/Software Engineer, Pratt & Whitney
Roseberry, Keith Software Technical Fellow, UTC Aerospace Systems
Varadaraju, Rakshith Software Engineer, Rockwell Collins

## Slide 3: Project overview
Using an Android Mobile Phone or a Raspberry Pi 3 B+ and a camera module, develop computer vision processing to perform the following functions
  Traffic Sign Recognition: Read traffic signs, most importantly speed limit signs, to determine appropriate driving behavior.
  Lane Departure Detection and Warning: Determine when the vehicle is departing from its travel lane and warn the operator. Requires recognition of a travel lane.
  Collision and Obstacle Avoidance: Detect obstacles in the path of the vehicle to predict collisions and warn the operator.

## Slide 4: System block diagram

## Slide 5: Extensibility
Object Oriented Programming: An OO architecture will help to create an encapsulated, modular software system that can be built on. OO architecture will also help distribute the work across the team members.
Event driven architecture: The software architecture will need to have modules that will monitor specific changes in the videos, and trigger functions to process those updates (for ex: speed limit sign comes into view)
Processing Optimizations: The target environment does not have very powerful processing power, making it very important to have optimized algorithms for video processing

## Slide 6: Modularity
Modularity: TBD – describe how the software should be internally partitioned to allow for multiple, simultaneous development and verification activities
Functions the system performs:
  Object identification: The system identifies objects of interest in the picture frame
  Object recognition: Once an object is identified, the system classifies it
  Notification: When a significant object (or event) is confirmed, notify the driver
TBD Details of each independent function: TBD

## Slide 7: Performance
Performance: TBD – describe performance characteristics that must be achieved
Needs to yield results fast enough to improve driver safety:
  Average driver reaction brake time is 2.3 seconds
    https://copradar.com/redlight/factors/index.html
  Average reaction time in general:
    0.25 seconds for visual stimulus
    0.17 for audio stimulus
    0.15 seconds for touch stimulus
    https://backyardbrains.com/experiments/reactiontime

## Slide 8: Safety & reliability
Safety: ADAS Level 1 (SAE) – Assisted Driving – Minimal Safety Impact
  System has no direct control of the vehicle
  False Alarms: Will increase driver workload, may result in anomalous driver reaction
Reliability: Degree to which the system is accurate, consistent and available
  As an aid, the system does not need to have strict reliability objectives
  Accuracy Goal: 75% of detections/alerts are valid and timely
  Consistency Goal: 90% of similar events are detected
  Availability Goal: Operational 90% of the time in normal daylight driving
    Excludes nighttime and bright sunlight/glare conditions

## Slide 9: Stakeholders, customers and impact
Customers: TBD – identify and describe the customers who will benefit from the system, and what benefits they may achieve.
Stakeholders: TBD – who else benefits from the system and in what way (auto manufacturers, insurance companies, family members, etc).
Impact: TBD – estimate an impact based on a baseline estimate of the number of collisions due to speeding, lane departure and obstacle interactions.

## Slide 10: Risks and challenges
New platform: team needs to learn and use the Android operating system and environment or the Raspberry Pi and Python; and computer vision algorithms
Performance: does the mobile phone platform or the Raspberry Pi provide enough performance to support this application?
Time: is there enough time in the 13 week semester to complete a significant portion of the project?
Distributed Team: Team will have to overcome geographic distances during integration effort

## Slide 11: Team Interactions
Team Meetings:
  Regular team meetings on Thursdays 7:00 - 9:00 PM Eastern
  Shorter "stand-up" meetings on Sundays 7:00 - 7:30 PM Eastern
Meeting room: SSW690 Google Meet room provided by Prof. Rowland
  Whatsapp for messaging in between meetings
  Email for longer messages
GitHub repository: https://github.com/Scarabyte/SSW690-Project

## Slide 12: We are… the Back seat drivers!
Source: http://unearthedcomics.com/comics/distracted-driving/ (Creative Commons License)